## Slide 1
GCT Camera Parameters
Summary Plots

## Slide 2: 1. Camera Pixels
Number of pixels per camera.
Value adopted: 2048
Status: Agreed

## Slide 3: 2. Camera Config File
Configuration file for the description of the camera with pixel types, positions and the circuitry for trigger decisions.

## Slide 4: 3. NSB
Number of photo-electrons per nanosecond per pixel due to nightsky background. Note that the number here takes into account all photo-electrons, including those not properly amplified or lost at the first dynode. A range of pixels can be given with nightsky background = (0-1236): 0.2, (1237-1854): 0.15. Alternatively, all pixels can be set with nightsky background = all: 0.2.
Status: To be derived by MC

## Slide 5: 4. SPE
File name for single p.e. response distribution.

## Slide 6: 5. Gain Variation
Fractional gain variation between different photodetectors after adjusting the voltage to have approximately the same gain in all channels. The parameter sets the Gaussian r.m.s. spread of random fluctuations, used as amplitude *= RandGaus(1., gain_variation).

## Slide 7: 6. PM Voltage Variation
Fractional high voltage variation, used to adjust the transit times (/ 1=p(V )). The parameter sets the Gaussian r.m.s. spread of random voltage fluctuations, V = RandGaus(1., pm_voltage_variation).

## Slide 8: 7. PM Transit Time
Total transit time of the photodetector at the average voltage.
Value Adopted: 4ns
Comment: This is a tunable MC parameter? Since arrival times are all normalized to the mean arrival time, is this relevant?
Status:

## Slide 9: 8. PM Transit Time Jitter
Jitter (Gaussian r.m.s. spread of random fluctuations) of individual photo-electrons in nanoseconds.

## Slide 10: 9. Photon Delay
An additional delay added to the arrival times of all photons at the photosensors.
Value Adopted: 5 ns
Comment: This is a tunable MC parameter?
Status:

## Slide 11: 10. QE
File name for the quantum efficiency curve.

## Slide 12: 11. QE Variations
Photoelectron collection efficiency variation (Gaussian r.m.s. spread of random fluctuations) between photodetectors.

## Slide 13: 12. Disc Bins
Number of time bins used for the discriminator/comparator simulation. The trigger simulation might cover a larger time window than the FADC signals.
Value Adopted: 120 time bins
Comment:

## Slide 14: 13. Disc Start
Number of time bins by which the discriminator/comparator simulation is ahead of the FADC readout.That is mainly relevant if different time windows are simulated for comparator inputs and digitised ADC values.

## Slide 15: 14. Default Trigger
The default meaning of a “Trigger” line in the camera definition file. If set to “Majority”, a “Trigger” line would indicate a “MajorityTrigger”, for “AnalogSum” it would indicate an “AnalogSumTrigger”,and for “DigitalSum” it would indicate a “DigitalSumTrigger”.

## Slide 16: 15. Pulse Shape
File name for pulse shape at the discriminator/comparator of an individual pixel. (DISC)

## Slide 17: 16. Discriminator Amplitude
Signal amplitude after amplifier per mean p.e. at the input of the discriminators/comparators. The unit is arbitrary (typically mV) but the same definition has to be used for the discriminator threshold. For the default value of 1.0, the unit is the average (not the most probable) amplitude of a single photo-electron, implying the same being used for thresholds and switching behaviour.

## Slide 18: 17. Trigger Pixels
Number of pixels required for single telescope trigger. With flexible camera definitions, this is the default number for the multiplicity required per trigger group. If the camera definition file contains a non-zero number in the definition of any trigger group, that number overrides the default

## Slide 19: 18. Teltrig Min Time
Minimum time of sector trigger over threshold. Used before telescope trigger.

## Slide 20: 19. Teltrig Min Sigsum
Minimum signal sum at sector trigger over threshold. Note that both the minimum time over threshold and the minimum signal sum have to be satisfied before a trigger is obtained. Normally, either of these values being non-zero should be sufficient.

## Slide 21: 20. Discriminator Sigsum Over Thresh
Integrated signal required over threshold. See also discriminator time over threshold above for combined effects. If discriminator time over threshold is not milliVolts, it scales accordingly.

## Slide 22: 21. Discriminator Var Sigsum over Thresh
Gaussian r.m.s. spread of discriminator sigsum over threshold (Pixel-to-pixel variation).

## Slide 23: 22. Discriminator Gate Length
Effective discriminator gate length. To achieve a comparator-type response this gate length must match the time over threshold below.

## Slide 24: 23. Discriminator Var Gate Length
Variation of gate length (Gaussian r.m.s.). In comparator-type response, this variable is not used but only discriminator var time over threshold.

## Slide 25: 24. Discriminator Rise Time
Rise time of the discriminator/comparator output. After the discriminator/comparator logical output is set true, the output signal linearly rises from 0 to 100% within the given time period.

## Slide 26: 25. Discriminator Var Threshold
Channel-to-channel variations (random Gaussian r.m.s.) of discriminator/comparator threshold.

## Slide 27: 26. Discriminator Hysteresis
The switching off of a comparator is normally with some hysteresis to avoid oscillating behaviour. As a consequence, the signal has to be below the threshold minus the hysteresis before it switches off.

## Slide 28: 27. Discriminator Fall Time
Fall time of discriminator/comparator output after the logical output is reset to false.

## Slide 29: 28. Discriminator Time Over Thresh
Time over threshold required before logic response switches to true. To achieve a comparator-type response this time must match the gate length above. Note that in addition a minimum signal integral discriminator sigsum over threshold may be set up. If so, both time over threshold and signal integral conditions have to be met before a ‘true’ output signal starts. Normally, either of them being non-zero should be sufficient.

## Slide 30: 29. Disc Var Time Over Threshold
Pixel-to-pixel variation of the time over threshold required before logic response switches to true.

## Slide 31: 30. Discriminator Output Amplitude
The nominal output amplitude of a pixel discriminator or comparator as seen at the sector (trigger group) coincidence unit.

## Slide 32: 31. Discriminator Output Var Percent
Channel-to-channel variation (Gaussian r.m.s.) of the output amplitude of a pixel discriminator or comparator.

## Slide 33: 32. FADC MHz
FADC sampling rate. A value of 250 (MHz or million samples per second) corresponds to an FADC time interval of 4 ns.

## Slide 34: 33. FADC Bins
Number of FADC bins to be filled. In the first place this means the number of bins simulated. The median of all Cherenkov light photo-electrons will be near 40% of the interval length, unless shifted with photon delay. If the photon delay is left at 0, this will also be used as the number of bins read out.

## Slide 35: 34. FADC Sum Bins
Number of bins summed up in ADC sum data or read out in sampled data. This number corresponds to the experimental length of the readout window. The start of the readout window starts fadc sum offset bins before the calculated time of the trigger, as long as the readout window fits fully in the simulated window. With peak sensing readout, the same interval is used for searching the peak signal.

## Slide 36: 35. FADC Sum Offset
Number of bins before telescope trigger where summing/reading of sampled data starts (see also description of fadc sum bins). With peak sensing readout, the same offset is used for setting the interval for the searching of the peak signal. For negative values, the summing/reading starts after the trigger.

## Slide 37: 36. FADC Pedestal
Nominal (F)ADC pedestal value per time slice.

## Slide 38: 37. FADC Amplitude
Peak amplitude at ADC/FADC (for high gain channel, if different gains are used). fadc amplitude are ADC counts maximum amplitude above pedestal (per time slice) for a photo-electron with average (not most probable) signal. This is after photodetector, preamplifier, cable, and shaper at the input of the ADC or FADC.

## Slide 39: 38. FADC Noise
Gaussian r.m.s. spread of white noise per time bin in digitisation (for high-gain channel, if different gains are used).

## Slide 40: 39. FADC Max Signal
The maximum value of the digitized signal per sample. For a typical 12-bit ADC this would be 4095.

## Slide 41: 40. FADC Pedestal Variation
Channel-to-channel (or pixel-to-pixel) variation of the pedestal per FADC time slice.